## Slide 1: VHDL 8 Practical examples
Part 1: 7-segment display ,
Part 2: A single board sound recorder
Part 3: Logic analyzer

## Slide 2: Part 1
7-segment LED display using VHDL

## Slide 3: Lab5
In this exercise, you are required to display a hexadecimal number (XY) of two digits. Digit X on the left is to be controlled by input switch [3:0], and digit Y on the right is to be controlled by input switch [7:4].
To display the digits and save power, we have to switch between the two digitals using the digital selection signal (ssdcat) at a rate around 500kHz.
Task1: Implement the above requirement to display the hexadecimal number XY.
Task2: In addition to task1, add an input button to the system, after the button is pressed, the two digits will count from the number (XY) you entered to FF(hex) at a rate of one number per second. When the display reaches FF(hex), it will repeat counting from XY to FF again, and so on.
https://www.beyond-circuits.com/wordpress/tutorial/tutorial4/
Digits X Y

## Slide 4: Define these in entity port declaration
entity sevenseg is
Port ( clk : in STD_LOGIC;
switch : in STD_LOGIC_VECTOR (7 downto 0);
ssd : out STD_LOGIC_VECTOR (6 downto 0);
ssdcat : out STD_LOGIC);
end sevenseg;
switch= user input switches
led: zedboard LED control
ssd: turn on/off individual LEDs in the active 7-segment
ssdcat: selects which 7-segment is active

## Slide 5: What is a 7-segment LED display?
Input Value | Segments Lit | ssd: Output Value
0 | A B C D E F | “1111110”
1 | B C | “0110000”
2 | A B D E G | “1101101”
3 | A B C D G | “1111001”
4 | B C F G | “0110011”
5 | A C D F G | “1011011”
6 | A C D E F G | “1011111”
7 | A B C | “1110000”
8 | A B C D E F G | “1111111”
9 | A B C F G | “1110011”
A | A B C E F G | “1110111”
b | C D E F G | “0011111”
C | A D E F | “1001110”
d | B C D E G | “0111101”
E | A D E F G | “1001111”
F | A E F G | “1000111”
ssd :turn on/off individual LEDs in the active 7-segment
ssd: turn on/off individual LEDs in the active 7-segment
https://www.beyond-circuits.com/wordpress/tutorial/tutorial4/

## Slide 6: Multiple 7-segment LED display method
Time multiplexing:
  Because LED consumes high power
  Make one 7-segment active at one time will save power.
  Activate the 7-segment on the right then left at a rate of 1KHz and so on.
ssdcat : selects which 7-segment is active

## Slide 7: VHDL for the 7-segment Input: clk (100MHz clock), digit(input code)
process(clk)
begin
case digit is
when "0000"=>ssd<="1111110";
when "0001"=>ssd<="0110000";
when "0010"=>ssd<="1101101";
when "0011"=>ssd<="1111001";
when "0100"=>ssd<="0110011";
when "0101"=>ssd<="1011011";
when "0110"=>ssd<="1011111";
when "0111"=>ssd<="1110000";
when "1000"=>ssd<="1111111";
when "1001"=>ssd<="1111011";
when "1010"=>ssd<="1110111";
when "1011"=>ssd<="0011111";
when "1100"=>ssd<="1001110";
when "1101"=>ssd<="0111101";
when "1110"=>ssd<="1001111";
when "1111"=>ssd<="1000111";
end case;
ssd: turn on/off individual LEDs in the active 7-segment

## Slide 8: Create a 1KHz clock from a 100MHz clk
If the clock frequency of clk is 100MHz
Create a 1 KHz (or 1ms-period) clock: ms_pulse
if rising_edge(clk) then
if (count=99999) then
ms_pulse <= not ms_pulse;
count<=0;
else
count <= count + 1;
end if;
end if;
ms_pulse (1KHz)
0.5ms

## Slide 9: Select input switch switches depending on ms_pulse
if ms_pulse='1' then
digit <= switch(7 downto 4)
else
digit <= switch(3 downto 0);
end if;
ssdcat <= ms_pulse;
ms_pulse (1KHz)
0.5ms

## Slide 10
library IEEE; --(Vivado ok)
use IEEE.std_logic_1164.all;
use IEEE.std_logic_arith.all;
use IEEE.std_logic_unsigned.all;
entity syn_counter is
port (
CLK: in STD_LOGIC;
RESET,CE, load, DIR: in STD_LOGIC;
DIN: in std_logic_vector(3 downto 0);
COUNT: inout std_logic_vector(3 downto 0));
end syn_counter;
architecture Behavioral of syn_counter is
begin
process( reset, clk) begin
if(reset = '1') then COUNT <= "0000";
else
if(clk'event and clk = '1') then
if(load = '1') then COUNT <= din;
else
if(ce = '1') then
if( dir = '1') then
count <= count + 1;
else
count <= count -1;
end if;
end if;
end if;
end if;
end if;
end process;
end Behavioral;
Example of a up/down counter (May be useful for the lab5 task2)

## Slide 11: Hints for lab5-task2
Hints for Task2:
  To build the 1Hz, 8-bit counter with an output (call it sec_count), you need a slower input clock (1Hz). You can use the similar method for ms_pulse (1KHz) discussed earlier, and the input clock can be the ms_pulse signal.
  When the input button is pressed, toggle an enable signal (e.g. counter_en) to enable/disable the 1Hz counter . Also, initialize the counter value with the value of the switches.
  In each second, if the counter is enabled, increase the counter value by 1. If the counter value reaches 0xFF(hex), reset it to the value of the switches.
  Check the state of both sec_count and counter_en to determine the source of the digit to be displayed (either from the 1Hz counter or switches).

## Slide 12: More hints for lab5 task2
  std_logic_vector cannot be incremented directly. Cast it to unsigned, signed or integer first.
  To convert signal type, you can refer to the figure in the appendix. For example, if you want to cast an integer sec_count to a 8-bit-unsigned std_logic_vector, you can type “std_logic_vector(to_unsigned (sec_count, 8))”.
  Avoid updating the same signal or I/O in different processes or else you will encounter multiple driver error (Remember processes within the same architecture run concurrently). However, it is safe to read them in different processes.
  If you receive error message “Poor placement for routing between an IO pin and BUFG” while running implementation stage, you may add “set_property CLOCK_DEDICATED_ROUTE FALSE [get_nets btn_IBUF]” in the constraint file to omit the issue.

## Slide 13: Part 2
General concept of memory

## Slide 14: Basic structure of a microprocessor system
CPU
Memory
Input/output and peripheral devices
Glue logic circuits

## Slide 15: A computer system with a microprocessor
Micro-
Processor (CPU)
memory
Peripheral devices: serial, parallel interfaces; real-time-clock etc.
Clock
Oscillator
Peripheral devices: serial, parallel interfaces; real-time-clock etc.

## Slide 16: Internal and external interfacing
CPU
memory
Peripheral devices: USB ports, Graphic card, real-time-clock etc.
Keyboard
mouse
Light,
Temperature
sensors
Effectors: such as
Motors,
Heaters,
speakers
Internal interfacing
External interfacing
Peripheral IO interface devices: such as USB bus, parallel bus, RS232 etc.

## Slide 17: CPU, MCU are microprocessors
CPU: Central Processing unit
  Requires memory and input/output system to become a computer (e.g. Pentium).
MCU: micro-controller unit (or single chip computer)
  Contains memory, input output systems, can work independently (e.g. Arm7, 8051).
  Used in embedded systems such as mp3 players, mobile phones.

## Slide 18: Memory systems
RAM/ROM

## Slide 19: Different kinds of Memory (RAM)
Random access memory (RAM): data will disappear after power down.
  Static RAM (SRAM): each bit is a flip-flop
  Dynamic RAM (DRAM): each bit is a small capacitor, and is needed to be recharged regularly
Since we only discuss static (SRAM) here, so the terms SRAM and RAM will be used interchangeably.

## Slide 20: Different kinds of Memory (ROM)
Read only memory (ROM)
  UV-EPROM
  EEPROM
  FLASH ROM

## Slide 21: UV-EPROM

## Slide 22: Flash memory
Or SD (secure digital card)
http://videoengineer.net/images/sdc32g2.jpg

## Slide 23: Memory is like a tall building Address cannot change; content (data) can change
Address content, e.g. A 32K-byte RAM
16-bit Address (H=Hex) | 8-bit content (data)
7FFF H | 35H
7FFF H | 23H
… | …
0ACD H | 24H
… | …
0001 H | 32H
0000 H | 2BH

## Slide 24: How a computer works?
Program is in memory
CPU
program counter (16 bit) [PC]:
Keeps track of program location
16-bit Address (H=Hex) | 8-bit content (data)
7FFF H | 35
7FFF H | 23
… | …
0ACD H | 24
… | …
0001 H | 32
0000 H | 2B (goto0ACD)
After power up
PC=0000H

## Slide 25: A simple program in memory
After power up, first instruction is in 0000H
An example
Address (H=Hex) | 8-bit machine code instructions (Hex) | 8-bit content (data)
0AC3 | 25 | Instruction j+3
0AC2 | 72 | Instruction j+2
0AC1 | 3B | Instruction j+1
0AC0 | 24 | Instruction j
… |  | …
0001 | xx | Instruction 2
0000 | 2B | Instruction 1
Register A

## Slide 26: Program to find 2+3=?
Address (H=Hex) | 8-bit content (data)
0AC3 | Send content of 0AC2 to output port
0AC2 | (so this is the answer for 2+3 =5)
0AC1 | Add 2 to Reg .A and save in next location
0AC0 | Save 3 into Reg. A
… | …
0001 | …
0000 | Goto address 0AC0 H
Register A

## Slide 27: CPU and Static memory (SRAM) interface Exercise: show the address space of the CPU and memory
Data bus is bi-directional DIN,DOUT are using the same bus (D0-D7)

## Slide 28: Exercises 8.1
A) What is the address space for an address bus of 24 bits?
B) How many address bits are required for a space of 4G bytes?
C) Why do most computers use 8-bit as the bit length of an address?

## Slide 29: Memory read/write
Timing diagrams
http://www.alliancememory.com/pdf/AS6C62256.pdf

## Slide 30: A read cycle tRC, from SRAM memory to CPU
Procedure:
  T0: setup address,
  T1: pull down /CE,
  T2: pull down /OE,
  T3: Dout data start to come out of memory, must be valid at T4
  T4: Pull up /CE
  T5: pull up /OE
T0 T1 T2 T3 T4 T5
All signals are coming out of CPU except Dout is from memory to CPU
Note:
  T2 can happen at the same time as T1 but not before.
  T5 can happen at the same time as T4 but not before.
For reading
(minimum 55ns)

## Slide 31: A write cycle tWC,, from CPU to SRAM memory
Procedure:
  T0: setup address,
  T1: pull down /WE,
  T2: pull down /CE
  T3: Din data start to come out of CPU, must be valid at T4
  T4: Pull up /CE and /OE at the same time
T0 T1 T2 T3 T4
Data bus is bi-directional
DIN,DOUT are using the
same bus (D0-D7)
Data bus is bi-directional
DIN,DOUT are using the
same bus (D0-D7)
All signals coming out of CPU
Dout is at high impedance all the time
For writing
(minimum 55ns)

## Slide 32: Exercises 8.2
(A): Redesign the CPU/SRAM interfaces circuit in figure 1 so that the address-range is 8000-FFFFH instead of 0000-7FFFH.

## Slide 33: Exercises 8.2B
(B): Redesign the CPU/SRAM interface circuit in figure 1 to add another SRAM to make the system occupies the whole 0000-FFFFH address-range.

## Slide 34: How to read timing diagrams ? part1
Valid bus
High-to-low, low-to-high uncertain regions

## Slide 35: How to read timing diagrams? part2
Float (High-Z) to uncertain then valid
T0 T1 T2

## Slide 36: Exercise8.3 , explain this timing diagram

## Slide 37: Address decoding

## Slide 38: Exercises 8.4
A CPU supports 128K-byte (has address pin A0-A16 = 17 pins, so 217=128K) of memory area.
Exercise2.4: How many 32K-SRAMs do we need?

## Slide 39: Exercise 8.5a
Address lines:
A15, A16
A0-A14
/WR
/RD
Data bus
D0-D7
Address decoder /CS0
/CS1
/CS2
/CS3
A0,A1
A CPU supports 128K-byte (has address pin A0-A16 = 17 pins, so 2^17=128K) of memory area. We need an address decoder to enable the (/CS) input of each SRAM. Complete the following diagram.
32K
SRAM2
/CS
A0-A14
/OE
/RD
D0-D7
32K
SRAM3
/CS
A0-A14
/OE
/RD
D0-D7
32K
SRAM4
/CS
A0-A14
/OE
/RD
D0-D7
32K
SRAM1
/CS
A0-A14
/OE
/RD
D0-D7

## Slide 40: Exercise 8.5b :Memory decode for a system with 128K-byte size using four 32-byte RAM chips , fill in the blanks.
A16,A15,……..A0 (17 bits) | Address range ( 5 hex.) | Range size
0 0xxx xxxx xxxx xxxx | 0 0000 - 0 7FFF H | 32K
0 1xxx xxxx xxxx xxxx | 0 8000 - 0 FFFFH | 32K
_ _xxx xxxx xxxx xxxx | 1 0000 - 1 7FFFH | __ K
1 1xxx xxxx xxxx xxxx | _ ____ - _ ____H | 32K

## Slide 41: Exercise 8.5c: fill in the address decoder truth table
A16 ,A15 | /CS0 | /CS1 | /CS2 | /CS3
0 0 |  |  |  | 
0 1 |  |  |  | 
1 0 |  |  |  | 
1 1 |  |  |  | 

## Slide 42: Address decode rules
Decode the upper address lines using a decoder.
Connect lower address lines directly to memory devices.

## Slide 43: Exercise 8.6
Fill in the modes (in, out, inout or buffer) of the input/output signal.
 | SRAM (memory) | CPU
address lines (A0-A16) |  | 
data lines (D0-D7) |  | 
/CS,/OE and /WE lines |  | 

## Slide 44: Exercise 8.7
Referring to the figure, what would happen if /RD of the CPU (connected to /OE) goes up before the data valid region occurs?
tRC
ADD
/CE
Or (/CS)
/OE
DOUT

## Slide 45: Exercise 8.8 :
Referring to the Figure,
if tAS=0ns, twc=100ns,tCW=80ns, give comments on the limits of tAW, tWP and tDW..
ADD
/CE
Or (/CS)
/WE
DIN
tWC
tCW
tAW
tDW
tWP

## Slide 46: Part 3
The Logic Analyzer

## Slide 47: The Logic Analyzer
Overall diagram
Xilinx based hardware
ARM7 board
RAM
Reset
Rec
Play
DA_in[7..0]
DA_out[7..0]
Serial port
Display waveform

## Slide 48: Memory (32K) interface
entity logic_rec is
Port ( clk40k_in: in std_logic;
reset: in std_logic;
rec, play: in std_logic; --user inputs
-- mem RAM bus
bar_ram_we27: out std_logic;
bar_ram_cs20: out std_logic;
bar_ram_oe22: out std_logic;
-- 32k-byte
ram_address_buf: buffer std_logic_vector(14 downto 0);
ram_data_inout: inout std_logic_vector(7 downto 0);
da_data_out: buffer std_logic_vector(7 downto 0);
da_data_in: in std_logic_vector(7 downto 0));
end logic_rec;

## Slide 49: Static memory (SRAM 32Kbytes) data pins
Diagrams are obtained from data sheet of HM62256B

## Slide 50: HM62256B Memory read timing diagrams

## Slide 51: HM62256B Write mode timing diagram

## Slide 52: Flow diagram
s_init
s_rec_address_change
s_rec_read_from_da_to_reg1
s_rec_we_cs_down
s_rec_writeto_da_ram
s_play_address_change
s_play_cs_oe_down
s_play_read_in_reg1
s_play_writeto_da
ram_address_buf =not all’1’
ram_address_buf =all’1’
ram_address_buf =not all’1’
rec=‘0’
play=‘0’
reset=‘0’

## Slide 53: Architecture
architecture Behavioral of logic_rec is
-- SYMBOLIC ENCODED state machine: Sreg0
type Sreg0_type is (s_init, s_rec_address_change, s_rec_we_cs_down, s_rec_read_from_da_to_reg1, s_rec_writeto_da_ram, s_play_address_change, s_play_cs_down, s_play_oe_down, s_play_read_in_reg1, s_play_writeto_da);
signal state_ram1: Sreg0_type;
signal data_reg1: std_logic_vector (7 downto 0);
begin
process (CLK40k_in,reset)
begin
if reset = '0' then --loop count
state_ram1 <= s_init;
elsif CLK40k_in'event and CLK40k_in = '1' then

## Slide 54: State s_init
case state_ram1 is
when s_init => --state: initial state
bar_ram_we27<='1';
bar_ram_cs20<='1';
bar_ram_oe22<='1';
ram_address_buf<="000000000000000";
ram_data_inout<= "ZZZZZZZZ";
if rec='0' then
state_ram1<=s_rec_address_change;
elsif (play='0') then
state_ram1<=s_play_address_change;
else
state_ram1<=s_init;
end if;

## Slide 55: State s_rec_address_change
-- signal record cycle starts here
when s_rec_address_change => -- state: rec01
bar_ram_we27<='1'; --make sure all ram pins up
bar_ram_cs20<='1';
bar_ram_oe22<='1';
if (ram_address_buf="111111111111111") then
state_ram1<=s_init;
else
ram_address_buf<=ram_address_buf+1;
state_ram1<=s_rec_read_from_da_to_reg1;
end if;

## Slide 56: States: s_rec_read_from_da_to_reg1 and s_rec_we_cs_down
when s_rec_read_from_da_to_reg1 => --state: rec02
bar_ram_cs20<='0';
bar_ram_we27<='1';
bar_ram_oe22<='1';
data_reg1<=da_data_in;
state_ram1<=s_rec_we_ce_down;
when s_rec_we_cs_down => -- state rec03
bar_ram_cs20<='0';
bar_ram_we27<='0';
bar_ram_oe22<='1';
state_ram1<=s_rec_writeto_da_ram;

## Slide 57: State s_rec_writeto_da_ram
when s_rec_writeto_da_ram=> -- state: rec04
bar_ram_we27<='0';
bar_ram_cs20<='0';
bar_ram_oe22<='1';
ram_data_inout<=data_reg1; --write to ram
--goback to record another sample
state_ram1<=s_rec_address_change;
--the ram control pins will be up at s_rec_address_change

## Slide 58: State: s_play_address_change
-- signal playback state machine cycle starts here
when s_play_address_change => -- state: play01
-- fill in the code for this state
To be done by students in the lab.

## Slide 59: Conclusion
Showed how to make a single board logic analyzer by VHDL
Can be modified for sound recorder, digital camera, mp3 player etc.

## Slide 60: Bonus Part
Using a FIFO (first in first out) memory

## Slide 61: FIFO RAM
Very similar to the previously introduced SRAM.
It has an internal counter to ensure the data are read and written in FIFO manner.
No need to specify address.

## Slide 62: Interface of FIFO RAM
SRCK, SWCK : clock for read and write, data out refreshed after each rising edge
RSTW, RSTR : signal to reset the read/write counter to the 0th address.
WE : write enable signal to take new data after each rising edge of the write clock

## Slide 63: Timing Diagram for FIFO RAM

## Slide 64: Timing Diagram for FIFO RAM

## Slide 65: Timing Diagram for FIFO RAM

## Slide 66: Timing Diagram for FIFO RAM

## Slide 67: Flow Diagram
Work to do in each state will be introduced in the following slides

## Slide 68: FSM states
State 0 : Initial state
  Transition : If record button is pressed, go to State 1
  If play button is pressed, go to State 3
  If no button is pressed, remain at State 0
  Things to do : 1. unable RAM writes
  2. dis-reset RAM write counter
  3. dis-reset RAM read counter
  4. stop RAM write clock
  5. stop RAM read clock
  6. stop counter clock
  7. reset counter

## Slide 69: FSM States
State 1 : Write counter resetting state
  Transition : Go to State 3 directly
  Things to do : 1. reset RAM write counter
State 3 : Read counter resetting state
  Transition : Go to State 4 directly
  Things to do : 1. reset RAM read counter

## Slide 70: FSM States
State 2 : Record state
  Transition : If stop signal is high, go to state 0
  else remain at state 2
  Things to do : 1. enable RAM writes
  2. start RAM write clock
  3. stop RAM read clock
  4. start counter clock
  5. dis-reset counter
  6. dis-reset RAM write counter

## Slide 71: FSM States
State 4 : Play state
  Transition : If stop signal is high, go to state 0
  else remain at state 4
  Things to do : 1. disable RAM writes
  2. stop RAM write clock
  3. start RAM read clock
  4. start counter clock
  5. dis-reset counter
  6. dis-reset RAM read counter

## Slide 72: Sound Recorder utilizing FIFO RAM
To be done in the lab.
A full skeleton code is given but need to fill in missing part in the FSM.

## Slide 73: Conclusion
Showed how to make a single board sound recorder by VHDL
Can be modified for digital camera, mp3 player etc.